## Slide 1
Introduction to ROS
Using robotic manipulators in ROS

## Slide 2: Challenge Pick and Place
Make a pick-and-place application, moving each object to the container with the matching color.
Python Code

## Slide 3: Challenge solution outline
Detect objects
Plan movement
Move
Grasp
Computer Vision
MoveIt Library
In simulation …
tf2
Not covered

## Slide 4: Xarm Model of a robotic arm

## Slide 5: tf2 Introduction
”tf2 maintains the relationship between coordinate frames in a tree structure buffered in time, and lets the user transform points, vectors, etc between any two coordinate frames at any desired point in time.”
Notes: Talk through the purpose of tf2

## Slide 6: tf2 Concept
Vision
Manipulator
Other robots
Common reference frame
Notes: Relate to a real scenario

## Slide 7: tf2 Static vs dynamic transform
Static Transform
  Meant to be used to define transformations that are not going to be changing during the operational time.
Dynamic Transform
  Used in scenarios where the relative position of the frame changes over time and needs to be updated
tf_static topic
tf topic
tf0
tf0
tf1
tf2
Notes: Explain different types of transform

## Slide 8: tf2 Computing a transform
# Initialize objects to store the transforms on them
self.tfBuffer = tf2_ros.Buffer() self.listener = tf2_ros.TransformListener(self.tfBuffer)
# Compute the transform between two frames at a given time
self.tfBuffer.lookup_transform("link_eef",data.frame,rospy.Time(),
rospy.Duration(0.5))
The Buffer object is used as a container for Listener to allocate the information retrieved from the function lookup_transform. In order to compute a transform, we need to provide the function with two frame names, destination and source, a time at which the transform is recorded and a time out. You can retrieve the transform between any two frames that can be connected though a tree.

## Slide 9: tf2 Sending a transform
# Populate the vector with the transformation of the system
t = TransformStamped() t.header.stamp = rospy.Time.now() t.header.frame_id = "sensor_frame" t.child_frame_id = "goal" t.transform.translation = ”some_translation" t.transform.rotation = ”some_rotation"
# Input the static transformation into the system
br = tf2_ros.StaticTransformBroadcaster() br.sendTransform(t)
# Input the transformation into the system
br = tf2_ros.TransformBroadcaster() br.sendTransform(t)
In order to send any transform within ROS the format of the transform must be TransformStamped(), which contains both a temporal reference and the transform object. Once the transform is defined it can be sent either as a static or dynamic transform by calling the appropriate sendTransform function from the broadcaster class.

## Slide 10: tf2 Debugging tools
The main tools used to analyze tf2 behavior are
  Command line tools
    rosrun tf2_tools view_frames.py
    rosrun tf tf_echo [base] [target]
  RQT_tree: A graphical representation of all the relationships within the network
  RVIZ: The temporal evolution of each transformation can be displayed in real time.
  Broadcasting transforms in your launch files

## Slide 11: MoveIt! Introduction

## Slide 12: MoveIt! Set Up
This wizard generates the planner code so that any manipulator can be commanded easily in ROS, either in simulation or in real life.

## Slide 13: MoveIt ! Wizard Summary
Load urdf models into the planner
  Create or modify config packages created for a given robot
Add self collisions between links
  Manage how links interact with each other
Add virtual joints to link the world with the robot framework
  Use auxiliar joints to relate the robot with the rest of the world
Add planning groups
  Divides the joints in groups for the planner to use when generating a path
Add passive joints
  Defines non-actuable joints
Add controllers
  Attaches ROS controllers to each of the joints
Input 3D information of the environment
  You can add depth sensors to detect obstacles that need to be avoided by the arm

## Slide 14: MoveIt ! Wizard Self-Collision
This set of options is used to prevent unnecessary collision simulation between links and avoid unrealistic collisions. For example, if two links are in contact, we don’t want our planner to treat it as a collision and thus it is included in this list.

## Slide 15: MoveIt ! Wizard Controllers
Screen devoted to add controllers to the joints of your robot. You already know how to do it working directly with urdf files, but it may be convenient to do it directly from this menu.

## Slide 16: MoveIt ! Wizard Robot Poses
This screen is used to preprogram poses in the planner. If you plan to travel to the same position repeatedly it is easier to encode it once and then access to it without using by its keyword.

## Slide 17: MoveIt! Wizard Perception
You can include perception to you planner by linking either a point cloud or a 3D camera. In that case obstacles detected will be represented as voxels in the planning space. Any plan derived will avoid those obstacles.

## Slide 18: MoveIt! Wizard Passive Joints
Passive joints are used to define non-actuated joints, which are not associated to any actuator. In that case the planner will consider the presence of that joint to derive paths and simulate its behavior, but won't provide control actions for them.

## Slide 19: MoveIt! Wizard Plan Groups
MoveIt! Allow subdivisions of joints into groups so that you can plan movements affecting only a subset of the robot, diminishing the computational time. It is common to, at least, define two subgroups so that arm and tool can be used independently.

## Slide 20: MoveIt! Rviz Interface
Most of the tools available in MoveIt can be applied to either real or simulated robot by sending commands through a visual interface coded in Rviz.
It is recommended to code your applications but is useful to test some of the movements beforehand.

## Slide 21: MoveIt! Rviz Interface
API to plan an execute movements though a user interface based on RVIZ.
Allows to configure different planning algorithms to drive the robot through the scene.
Tool to use the robot without having to code, only using visual tools.

## Slide 22: MoveIt! Rviz Interface
Main window of the API, allows setting up the connection to a real robot, configure the planner by choosing from a list of available algorithms and set up the center of a workspace.

## Slide 23: MoveIt! Rviz Interface
The ”Plan” window is used to limit some aspects from the planner, to adapt its performance to the needs of the user. Once the planner is set up you can either plan or execute a path for any of the groups defined in the set up step.

## Slide 24: MoveIt! Rviz Interface
This window allows to place obstacles within the navigation space. Similarly, to what we’ve already seen in the setup phase, this option creates areas in the space that are avoided by the planner.

## Slide 25: MoveIt! Rviz Interface
Menu used to set the value of any joint within the current operational group to a given value. It also allows to set up the value at which the null space is explored, which refers to the number of redundant positions that are explored.

## Slide 26: Activity Controlling the robot through the interface
Run the Rviz interface using the package generated in the previous activity.
Using the appropriate commands, navigate through the environment and check that the plans avoid the highlighted area.
Rviz Interface
World

## Slide 27: Challenge Proposed scheme
Planning node – MCR2
Node where we use tf2 to extract info from the world and drive the robot.
Movement node - you
Node where we use MoveIt to execute the movement.
Code structure